## Slide 1: ARDUINO MASTER CLASS
02
Installing Software & Libraries | Programming Arduino

## Slide 2: 2 AGENDA 01 02 03 04
Arduino IDE
Installing Arduino Libraries
Installing Arduino IDE & Exploring
Arduino Programming

## Slide 3: ARDUINO IDE
The Arduino Integrated Development Environment is a cross-platform application that is written in functions from C and C++.
It is used to write and upload programs to Arduino compatible boards, but also, with the help of third-party cores, other vendor development boards.

## Slide 4: INSTALLING ARDUINO https://www.arduino.cc/en/software

## Slide 5: PROGRAMMING ARDUINO – EXPLORING IDE
Open Arduino IDE
Select File > New
New blank file will open as shown in Fig.
Code should be written on this program space.
After writing the code, it should be compiled and burn to the Arduino board via COM port through USB serial.

## Slide 6: BASIC PROGRAMMING SYNTAX- ARDUINO If - Else For
if (someCondition)
{
// do stuff if the condition is true
}
else
{
// do stuff if the condition is false
}
for (initialization; condition; increment)
{
// statement(s);
}

## Slide 7: BASIC PROGRAMMING SYNTAX- ARDUINO while Switch
while (condition) {
// statement(s)
}
switch (var) {
case label1:
// statements
break;
case label2:
// statements
break;
default:
// statements
break;
}

## Slide 8: HARDWARE CONFIG SYNTAX - ARDUINO pinMode digitalRead digitalWrite analogRead analogWrite delay serialRead serialWrite

## Slide 9: INBUILT LED BLINK - ARDUINO void setup() { pinMode(13, OUTPUT); } void loop() { digitalWrite(13, HIGH); delay(1000); digitalWrite(13, LOW); delay(1000); }

## Slide 10: INTERVIEW QUESTIONS What is mean by IDE? What are the software structure functions? In which language Arduino software was written?

## Slide 11: THANKS!

## Slide 12: Q & A SESSION